## Slide 1: Control Card Block Diagram
PSRAM
FPGA
RPi Zero
RP2040
FTDI USB
PSRAM
Detector Backplanes
Source Backplane
Detector Backplanes
Detector Backplanes
Detector Backplanes
UART + SWD + 1 GPIO
9 GPIO (incl RPi 0 SPI)
Spare Con.
6 GPIO
12 GPIO
UART with RTS/CTS
7 GPIO
Spare Con2
4 GPIO
Aux ADCs
6 GPIO
2x6 GPIO
15 GPIO UART with CTS/RTS or parallel data
2 GPIO (incl I2C)
4 Backplane Connectors
Per Connector 17 GPIO
(5 common + 4x3 direct)
1 Backplane Connector
21 GPIO
(8 rows + 4x2 columns + 3 power select + 2 spare)

## Slide 2: FPGA Firmware Block Diagram
UART Rx
UART Tx
18 x 1024
Acquisition Sequence RAM B
27 x 1024
State Sequence RAM A
Source Backplane
8 rows
8 columns
3 power select
Program
Counter A
Program
Counter B
1 Trigger
1 Trigger Status
1 End Cycle
16 Board Select
+1
FTDI USB
Host PC
USB
Config
FSM
Acq
FSM/MUX
UART Rx
Aux ADC Interface
Detector Backplanes
FIFO
UART with RTS/CTS
Status Registers
FPGA

## Slide 3: RAM Data Formats
RAM A: State Sequence
End: 1 if last state in sequence: will jump to state 0 next; 0 otherwise: will jump to state i+1 next
X Reserved: reserved for later use
Status: ‘1’ send status packets instead of regular light level packets; ‘0’ send regular packets
Power: select LED power level. 0b001: high power, 0b010: mid power, 0b100: low power, 0b000: off (dark state)
Column select: Select column of LED to be illuminated. Even numbers correspond to XXX nm, odd numbers to YYY nm. This is selecting source boards.
Row select: Select row of LED to be illuminated. This is switching between LEDs in a source board
 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
state 0 | end | X reserved |  |  |  | stat | power | stat | power | X reserved |  | column select | data source |  | packet count |  |  | Lsr id |  | row select |  |  |  |  |  |  | 
⁞ |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
S 1023 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RAM B: Acquisition Sequence Sequence
End: 1 if last state in sequence: will jump to state 0 next; 0 otherwise: will jump to state i+1 next
X Reserved: reserved for later use
Acq Trg: Transition form ‘0’ to ‘1’ will trigger the acquisition of one sample in the detector boards
End Cyc: Transition form ‘0’ to ‘1’ will cause the detector boards to move the current measurements to the transmit buffer, and reset the sample sums to 0
PC Tx Trg: Program counter A transmit trigger. Transition form ‘0’ to ‘1’ will cause the current program counter A (state) to be transmitted
Aux Tx Trg: Auxillary transmit trigger. Transition form ‘0’ to ‘1’ will cause the current auxiliary ADC values to be transmitted.
DetB Rx En: Enable reception of data from the detector board selected by UART Rx Mux. Sets CTS for the selected board.
UART Rx Mux: Selects from which detector board to receive data.
 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
State 0 | End | X | X | X | X | X | X | X | Acq Trg | End cyc | PC Tx Trg | Aux Tx Trg | DetB Rx En | X | UART Rx Mux |  |  | 

## Slide 4: Status Register Format
Status Register
Clk Div: Clock divider setting. RAM B state period = ClkDiv*8/96MHz
Rst PC A: Reset program counter A to 0
Rst PC B: Reset program counter B to 0
Rst Clk Div: Reset clock divider to 0
Rst DetB: Reset the microcontroller on the detector boards. (Will pull RUN pin low.)
Run: ‘1’: the clock divider and program counters A and B will run. ‘0’ divider and counters stop at the current location. LED power will be set to 0.
 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | VN22Clk en | VN3P4 en | VN22 en | V9P0 en | V5P1src en | V5P1RPi en | V5P1B23 en | V5P1B01 en | Clk Div |  |  |  |  |  |  |  | X | X | X | Rst PC A | Rst PC B | Rst Clk Div | Rst DetB | Run

## Slide 5: Command Format
Command sequence
End: 1 if last state in sequence: will jump to state 0 next; 0 otherwise: will jump to state i+1 next
 | byte[0] | byte[1] | byte[2] | byte[3] | byte[4] | byte[5] | byte[6]
 | 255 | addr[1] | addr[0] | cmd[3] | cmd[2] | cmd[1] | cmd[0]

## Slide 6: Output Data Format
Header from FPGA [254]
State number
Header from Detector board [253 252]
Sample counter
(Status flag?)
Payload
(Checksum)